## Slide 1: Different technologies used for proteomics measurement
EPI-OMICs Journal Club
9-Feb-2023
Keyong Deng
Department of Clinical Epidemiology

## Slide 2: Background
    ~30,000 proteins make up the human proteome
    Medications or lifestyle changes cause shifts in the proteome
Phenotype
Genome
Proteome
Transcriptome
Metabolome
…
    Central dogma

## Slide 3: What’s Proteomics?
Discover potential biomarkers (also those previously unrecorded)
    prostate-specific antigen (PSA) for cancer diagnosis
    …
Identify druggable targets
Identify novel pathways involved in the process of disease
Proteomics is a high throughput way to measure all proteins in a cell or tissue by using mass spectrometry or other methods
Why do we use Proteomics?
Proteins

## Slide 5: Technology development
Western blot
Enzyme-linked immunosorbent assays (ELISA)
Immunohistochemistry
Immunofluorescence
Mass spectrometry
Aptamer-based array
Immunoaffinity array (proximity extension assay-based)
Low throughput
High throughput

## Slide 6: Four common proteomic technologies
Mass spectrometry (MS)-based
    LC/MS-MS
    Fragments proteins and measure Mass-to-charge ratios
Protein microarray
    Antibodies with fluorophore
Aptamer-based
    SOMA (slow off-rate modified aptamers )scan platform
    Oligonucleotides increase sensitivity & specificity
Proximity extension assay (PEA)-based
    OLINK platform
    Paired DNA-conjugated antibodies

## Slide 7: 1. MS-based proteomics
MS has three basic components:
Ion source
    Electrospray ionization (ESI)
Mass analyser: separate ions by their mass-to-charge ratios (m/z)
    Quadrupoles, time-of-flight (TOF), Orbitrap
Detector

## Slide 8: 1. MS-based proteomics
Top-down strategy
    Full-length protein -> problems: heterogeneity of proteins
Bottom-up strategy
    Peptides (digested protein)
    Coverage more than 10,000 preteins
  Protein digestion -> peptide purification -> separated by Liquid chromatography ->
  Ionized by electrospray (ES) -> Analysis in MS

## Slide 9: 2. Aptamer-based proteomics
Aptamers are short, single-stranded oligonucleotides (DNA) that can selectively bind to a specific protein target
Binding (SOMAmers + samples)
SOMAmers contain biotin (B) and photo-cleavable linker (L) and fluorescent tag at 5’ end,
Binding with proteins
SOMAmers captured onto a bead coated with streptavidin (SA) which binds biotin
Proteins are tagged with NHS-biotin
UV light cleaves the linker and SOMAmers released
SOMAmer-protein complexes captured onto new SA coated beads by protein biotin tag
SOMAmers released from complexes into solution at high pH
Remaining SOMAmers are quantified by hybridization to microarray

## Slide 10: 3. Proximity extension assay (PEA)-based proteomics
DNA-conjugated antibodies bind to their target protein
Antibodies with correct matched pairs hybridize and extended by DNA polymerase
Unique barcode-regions identify each sample and protein and adaptors
DNA tags extended & amplified
Hybridized DNA strands: amplified and measured using qPCR or NGS
Using paired, nucleotide-labelled antibody probes for multiplexing of proteins at high sample throughput

## Slide 11: Which one should we choose?
Q: What are important factors?

## Slide 12
It depends on
Budgets! ($.$, always important)
Sample size or power calculation
Research question (if focus on posyttranslational modifications)
Sample consumption (if difficult to get)
Dynamic range (if huge or not)
…

## Slide 13: Technical factors influence selection
 | MS | Aptamer | PEA
Sample throughput | Low (untargeted) to moderate (targeted) | High | High
Analyte multiplex | All proteins in sample: 10 to >5000 | >1300 proteins | Depends on different panels
Sample volume | 30ul (targeted) to 100s of ul | 65ul | 1ul to 100s of ul
Dynamic range | High and medium-abundance proteins | Wide (mg/mL to pg/mL) | Wide (down to fg/mL)
Reproducibility | Modest | Good | Good
Quantification | Relative, targeted labeling for absolute | Relative | Absolute or relative
Characterization of PTMs | Yes | NO | NO
Bioinformatics | Multiple software available | Easy | Easy

## Slide 14: What will happen while using different methods?
A substantial number of proteins are not correlated across platforms
Aptamer-based VS immunoassay
Aptamer-based VS Olink
Some proteins are not correlated when using these methods
Notes: Comparison of available platforms offers an opportunity for high-throughput assessment.

## Slide 15: Conclusion
 | Advantage 😃 | Disadvantage ☹
Mass spectrometry (MS)-based | Results can be compared with databases available online Allows for discovery of new proteins Allows for analysis of post-translational modifications | Methods may result in damage to analyte protein of interest (fragmentation by ionization source) Sensitivity affected by presence of more abundant proteins (albumin)
Aptamer-based | Strong affinity for target proteins even at low concentrations Growing aptamer library increases number of proteins in the proteome | Involving multiple steps (aptamer design, multiple washings etc.,) may introduce human error Limited by the aptamers in libraries Limited ability to detect proteins with post-translational modifications
PEA-based (OLINK) | Minimal cross reactivity Just require a little volume of sample (such as 1ul) | Limited to currently developed panels Limited ability to detect proteins with post-translational modifications Limited by oligonucleotide libraries

## Slide 16
1. Overview of different proteomic methods
2. Characteristics of the principal proteomic methods
3. Factors need to consider while selecting
Review

## Slide 17: Glossary of some Proteomics Terms
Coverage:
    total proportion of protein identified from a complex mixture
Dynamic range:
    the largest and smallest abundance of proteins in a mixture
Sensitivity
    measure of assay ability to capture analytes with low abundance
  Specificity
    measure of assay ability to measure particular analyte rather than others

## Slide 18
Thanks
Q&A